| Titel | Feedback Hall-ONLY FBTYPE 11 | Device: | S300 / S700 |
| --- | --- | --- | --- |
| Number |  | Module: | Firmware |
| Author | Ibrahim Albach Translation: Niclas Will | Firmware | V 5.80 |
| Date | 03.02.2015 | Function | Comissioning of Hall only |
| Blatt | von |  |  |

# Hall-ONLY as a Feedback:

Hall-ONLY as a Feedback has some specific characteristics. This document aims to enhance the comprehension of Hall-ONLY.

## Hall-segments:

For any electrical revolution (2 motorpoles) the Hall-sensor gives out 6 electrical pulses. This means 60° (of an electrical revolution) per pulse.

For further information visit Hall Geber in our Wiki.

## Hall-ONLY feedback with low speed:

The drive receives a new position information by hall-sensor every 60°. If we assume that the motor has 6 poles, one mechanical revolution = 3 electrical revolutions. This means,  every 20° we receive a new Hall-Position: 0°, 20°, 40°, 60°,…, 340°.

This information is not enough for a reasonable controlling in the lower speed range.

For this reason there are two controlling-methods, which are applicable depending on the velocity-feedback.

In the lower speed range (velocity-feedback is lower than SLISWITCH) the motor is controlled sensor-less. Above the velocity in SLJSWITCH the drive uses the position information from the hall-segments (commutation, velocity, position)

The following concept of controlling are integrated in S300 / S700:

- Stepper mode, U/F operation:

The drive operates like a stepper drive, U/F curve.

This mode is activated by SLMODE 1.

- HF mode (High frequency injection)

This mode is activated by SLMODE 0. It just exists for compatibility reasons and will not be developed further.

## ASCII parameters for Hall-ONLY:

- SLMODE: With this parameter you can choose between Stepper Mode (U/F) or HF function. This function is used in the lower speed range only.

  - SLMODE 0: Enable HF mode. In this mode TEN must be zero. If not, no torque will be applied.

  - SLMODE 1: Enable stepper mode(U/F). This mode is recommended.

- TEN: is set internally by firmware if SLMODE =1. Depends on velocity feedback and SLMODE:

  - TEN 0: just in SLMODE 0.

    - V < SLJSWITCH HF active.

    - V > SLJSWITCH Hall-information is used for controlling .

  - TEN 1: V < SLJSWITCH: U/F active.

  - TEN 2: V > SLJSWITCH: Hall-information is used for controlling.

- SLJSWITCH: Threshold value for lower speed range. Default 500 RPM.

- SLTSWITCH: Transition time from lower speed range to higher speed range in ms. Default value: 200ms. The motor continues using SLMODE, before hall-sensor based controlling is activated.

- DRVCNFG4.Bit11: Improved calculation of the current speed in hall-only mode. This function is not active by default (for compatibility reasons), but should be used in new hall-only applications.

## OPMODE 2/3 Torque mode

Torque mode cannot be used with Hall-only. Even without a torque-command, the motor  has a torque (if drive enabled), because the U/F or HF function is active in the low speed range.

Commutation finding ZERO, MPHASE:

MPHASE is calculated by the ZERO function in OPMODE 2, like all other feedbacks.

Because Hall-Only only has one impuls per 60° (electrical), MPHASE has an accuracy of ±30° (electrical). The drive commutates in the low speed range sensorless and uses MPHASE and sensor-signals for commutation in the normal speed range.

Fast comissioning:

- DRVCNFG4.Bit11= 1

- SLMODE 1					//in SLMODE 1 TEN is controlled automatically

In SLMODE 0 TEN has to be 0!

- SLACCMAX 100 rpm/s				//Can be increased when in use.

- ACC=DEC=DECDIS=DECSTOP=500 rpm/s		// Can be increased when in use.

- MRESBW 50					//between 30 and 100

- ….?